## Slide 1
Lecture on
Modelling and Implementing Slip Target Shaper for Traction Control in F1 Application
Ing. Ugo Pattacini
Thales Alenia Space Italia S.p.A.
(formerly Embedded SW Developer at Toyota Motorsport GmbH)
14 September 2007
Italian Institute of Technology

## Slide 2
Introduction to Vehicle Dynamics and Traction Control
  Tyre model and PIS controller
Input Shaping Background
  Posicast, Robustness, Pole-Zero Analysis
Shaper Design and Implementation in dSPACE TargetLink
  Model inspection and analysis of production code
Embedding Production Code within Toyota F1 RT SW
  TF1 HW/SW Architecture
Jerez test reports on Slip Target Shaper
Shaper’s automatic tuning through GA
Table of Contents

## Slide 3
Vehicle Dynamics
z
Direction of Wheel Heading
(upward)
Overturning
Moment Mx
γ
Wheel Plane
Lat. Force Fy
Long. Tractive
Force Fx
Camber
α
Slip Angle
Road Plane
Spin Axis
Aligning
Torque Mz
Rolling Resistance
Moment My
SLIP ANGLE (radiant)
The car Slip Angle is the angle between the direction of travel of the car and the longitudinal axis.
Slip angle becomes high with high lateral acceleration and low speed.
Linear interpolation on ai allows the calculation of  for all velocities.

## Slide 4
Vehicle Dynamics
VERTICAL FORCES on the WHEELS (N)
Vertical force on a wheel is a combination of the force measured by the pushrod sensor (which are relative sensors, i.e. they see a deviation from the static load state of the car) and the wheel specific component of the dynamic mass of the car (dependent on the longitudinal and lateral acceleration and the characteristics of the suspension set-up).
FZRR = Vertical load on the rear right wheel
FRODRR = Rear right push rod force (variable, available in ECU)
RPMR = Rear push to wheel force ratio (constant, available in ECU)
MST = Static mass of car (constant, available in ECU)
MST_B = Front to rear static mass balance (constant, available in ECU)
AY = Lateral acceleration (variable, available in ECU)
AX = Longitudinal acceleration (variable, available in ECU)
RKYZ = Rear anti-roll coefficient (constant, available in ECU)
RKXZ_E = Rear anti squat coefficient (constant, available in ECU)

## Slide 5
Vehicle Dynamics
SLIP RATIO (%)
Definition of longitudinal Slip Ratio SX
= angular wheel speed
= effective rolling radius
= speed of axle relative to road
 = slip angle
As the slip angle is small (less than 5°), it has a negligible effect and can be ignored.
LONGITUDINAL TYRE MODEL
The effectiveness of the tyre model will depend upon how well it matches with the actual tyre performance. This is heavily reliant upon the constants used in the model:
17 fitting constants
7 tuning constants
1 scaling constant
The fitting constants and scaling constant are chosen by tyre supplier to match test data and the tuning constant can be used to adapt the model to different track/weather conditions.

## Slide 6
Vehicle Dynamics
Longitudinal tyre force vs. slip ratio, for varying vertical load (1) and slip angle (2).
1
2
The output of the model is the longitudinal force produced by the tyre, which is a function of slip ratio, slip angle and vertical force.
The aim is to control the slip ratio in order to achieve the maximum torque allowed by the car and the grip conditions.

## Slide 7
Traction Control
TRACTION CONTROL
Traction Control tries to limit the torque transmitted to the road to an optimal value giving the best acceleration. It gets enabled typically during corner exit.
The torque based traction control strategy sends to the torque control module a torque demand (made of a predictive term and a reactive term) and a torque reserve factor (to limit the amount of throttle reduction).
The predictive term is based on the max transmittable torque from the tyres to the road (=f(α, FZ)) and the power train inertial torque.
The reactive term is the output of a slip ratio controller trying to hold a slip ratio target = f(VCAR, |AY|).
C
lutch
E
ngine
L
ayshaft
M
ain
shaft
CWP
F
inal
D
rive
R
ear
T
yre
M
ainshaft
speed
sensor
L
ay
shaft
speed
sensor
S
1
2
3
4
5
1
2
3
5
6
7
6+1 configuration
6
4
7 gear configuration
From the torque transmitted to the road (Plant output) to the Engine Torque (the controlled variable)

## Slide 8
Traction Control
PREDICTIVE TERM (feed-forward)
The predictive torque demand is made of the average of the optimum torque at the wheels (Topt) related to the engine through the drive train ratios. The predictive torque is limited to the driver demand to allow better alignment to the real grip level even for bad μ settings.
The Friction coefficient μ(α) is calculated relying on baseline maps. It is the most critical parameter to be tuned, leading to several different strategies for self-adaptation (corrections on slip ratio error, Friction Ellipse)

## Slide 9
Traction Control
REACTIVE TERM (feedback)
The reactive torque demand is the output of a PIS slip ratio controller, which tries to hold the slip ratio target close to the optimum value SXopt in order to ensure the best grip.
SXopt is a complex function of VCAR, AY and slip angle:
where S0, K, N and C are functions of VCAR
PIS implemented in F1 TC (TOYOTA)
(Proportional+Integral+Smoothing) in anti-windup configuration

## Slide 10
Traction Control
PIS in action
Initial snap overshoot in the slip ratio brings about a reduction in the achievable speed during corner exit, causes also tyres degradation and a temporary loss of car stability for the driver.
overshoot
Slip Target Shaper represents an attempt to cope this issue by shaping the slip command at the input stage of PIS controller

## Slide 11
Input Shaping Theory
INPUT SHAPING
The process of input shaping is a valuable method for controlling systems with performance limiting vibration.
The first shaper proposed by Smith[1] was a simple technique to generate non-oscillatory response from a lightly-damped system subject to a step input. This was achieved by exciting two transient oscillations so as to result in constructive cancellation of the oscillations. (Posicast)
Applications: chemical process, spacecrafts, flexible systems (cranes, robots, …)

## Slide 12
Input Shaping Theory
Posicast solution
Problem: find the input sequence with some constraints to obtain a bounded solution
The impulse sequence is convolved with any desired command signal.
If the impulse sequence causes no vibration, then the convolution product will also cause no vibration.

## Slide 13
Input Shaping Theory
Robustness to Modelling Errors
The amplitudes and time locations of the impulses depend on the system parameters (ω and ζ). If there are errors in these values (and there always are), then the impulse sequence will not result in zero vibration (ZV).
This problem can be visualized by plotting a sensitivity curve that shows the amplitude of residual vibration as a function of the system parameters.
Insertion of additional constraints to improve robustness: ZVD, EI.
ZVD (Zero Vibration Derivative)
EI (Extra-Insensitive) with frequency sampling

## Slide 14
Input Shaping Theory
Pole-Zeros Analysis
A useful method for explaining the effectiveness of shaped command signals is to use pole-zero analysis to determine the location of the zeros and/or poles of the command shaping process.
If a shaped command contains zeros near the poles of the system being controlled, then the vibration from those poles is attenuated by the zeros of the command.
ZV shaper places a single zero over each of the flexible poles. If the poles deviate from their modelled locations, the attenuating effect of the zeros decreases.
ZVD shaper places two zeros over each pole. When a pole deviates from its modelled location, the two zeros have a greater attenuating effect.
EI shaper place zeros at nearby locations, taking into more account the uncertainties in the model.
Zero Locations of Typical Input Shapers
The zero separation of EI extends the attenuating effect to a larger area.
Adding more zeros makes the shaper more robust. We pay it with increased rising time.

## Slide 15
Shaper Design
Shaper Design through Pole-Zero Analysis
The shaper transfer function can be expressed as:
where p and p* represent a pair of complex poles and n is the number of flexible modes being targeted for elimination. The transfer function must have as many poles at z = 0 as zeros in the numerator so that the shaped command will be causal.
One drawback is that the shaper can contain large positive and negative valued impulses capable of saturating the actuators.
This difficulty can be avoided by using an artificially coarse sampling rate. This approach can be thought of as inserting zero-amplitude impulses at the true digital time step between finite amplitude impulses at some multiple of the sampling period.
Methods for selecting this surrogate sampling period are usually based on the constraint that all the impulses must have positive values. To demonstrate such a method, an example using the six-step procedure is reproduced here.

## Slide 16
Shaper Design
Six-step Procedure[2]
Goal: Design a shaper for a system with modes at 1 Hz and 4 Hz and damping ratios at each mode of 0.1.
Step 1: Identify the unwanted system poles and cover them with zeros in the z-plane.
z = esT
p1, p1* = e-0.2 πT ± j1.99 πT
p2, p2* = e-0.8 πT ± j7.96 πT
Step 2: Insert additional zeros for robustness.
(For simplicity, it will be assumed that a single zero at each pole is adequate for this example)
Step 3: Construct the shaper transfer function.

## Slide 17
Shaper Design
Step 4: Calculate the resulting impulse sequence.
h(t) =C [ δ(t)+ a1 δ(t -T)+ a2 δ(t -2T)+ a3 δ(t -3T)+ a4 δ(t - 4T)]
where parameters ai are function of sample time T.
Step 5: Plot the impulse amplitudes as a function of T and select a sequence that meets actuator constraints.
for T=0.147 all ai are positive
Step 6: Normalize amplitudes.
Typically C is set in order to scale the amplitudes to sum to unity.
h(t) = 0.516 δ(t)+0.042 δ(t -0.147)+
0.237 δ(t -0.441)+0.205 δ(t -0.588)

## Slide 18
Shaper Implementation
dSPACE TargetLink Environment
Production code generation directly from MATLAB/Simulink/Stateflow.
ANSI C code with the efficiency of handwritten code.
Optimizations for individual processors.
Built-in simulation and testing.
Key Benefits
Connect function development and code generation easily.
Converting graphical models directly into production code ensures perfect consistency between model and code at all times.
TargetLink’s code generation is deterministic.
Every step can be tested against the specification via the built-in simulation features.
Time and costs reductions.
Real Time Workshop Embedded Coder is the MathWorks answer to dSPACE.
(It came available later on the market).

## Slide 19
Shaper Implementation
Goal: implement the following Slip Target Shaper
h(t) = a1δ(t)+ a2δ(t -T1)+ a3 δ(t -T2)+ a4 δ(t -T3)+ a5 δ(t - T4)+…+ a16 δ(t - T15)
f32_Traction_SlipShaperC is a vector of 16 shaper’s coefficients as addressed six-step procedure. The sum of elements should be 1 in order to track the target perfectly.
u32_Traction_SlipShaperT is a vector of 15 shaper’s time references expressed in milliseconds. The sum of elements shall not exceed 512 ms, that is the internal buffer size.
As the size of coefficients vector is 16, the maximum number of modes it is possible to work on is 7.
Triggering Conditions
When enabled Shaper always performs filtering. It gets armed and triggers a “shaping reset” only when the slip is greater than a specified threshold, that is, once triggered, Shaper restarts filtering the target as it would have begun from current value of slip. Therefore, the actual difference between target and slip is considered the big step to be filtered out.
Disabling Conditions
Shaper is disabled as soon as the shaped target gets closer to the unshaped form (threshold). This aims at avoiding introducing phase lag and offset error on target when Shaper has already accomplished its work.

## Slide 20
Shaper Implementation
Browse Model
Browse C modules
Traction()

## Slide 21
TF1 HW Architecture
μC
Slavebox R
μC
Slavebox L
TDC 1
TDC 9
TDC 4
TDC 8
TDC 3
TDC 7
TDC 2
TDC 10
TDC 5
TDC 1
TDC 6
Engine Synchronous (Flywheel)
μC
Gearbox
DSP 1
DSP 2
DSP 3
DSP 4
DSP 5
μCOMM
SDRAM
CPM
SDRAM
FLASH
ETH
ARC
ARC
Masterbox
ARC
Adv Red, Ign Cuts
Adv Red, Ign Cuts
Throttle Demand
RT clock
TC
TRQ
Wheel Speed
Engine Revs
Torque Demand
DRV, TC, GS, CC

## Slide 22
TF1 RTOS Architecture
#msg_TS5_TS2_TrqDem, STEP11_TS5, STEP11_TS2;
f32_Traction_TorqueDem, IN_TS5.f32_Traction_TorqueDem, 1, 0;
f32_Traction_TorqueRes, IN_TS5.f32_Traction_TorqueRes, 1, 0;
f32_RpmLim_TorqueDem, IN_TS5.f32_RpmLim_TorqueDem, 1, 0;
f32_RpmLim_TorqueRes, IN_TS5.f32_RpmLim_TorqueRes, 1, 0;
f32_CruiseCtrl_TorqueDem, IN_TS5.f32_CruiseCtrl_TorqueDem, 1, 0;
f32_CruiseCtrl_TorqueRes, IN_TS5.f32_CruiseCtrl_TorqueRes, 1, 0;
u32_Launch_State, IN_TS5.u32_Launch_State, 1, 0;
f32_Launch_ThrDem, IN_TS5.f32_Launch_ThrDem, 1, 0;
f32_Launch_TorqueDem, IN_TS5.f32_Launch_TorqueDem, 1, 0;
Message Description File
dSPACE TargetLink
void INT_1ms_slot1(void) {
GetMsg(&msg_TS5_TS2_TrqDem);
…
Torque();
…
}
DSP 2
void INT_1ms_slot0(void) {
…
Traction();
…
SendMsg(&msg_TS5_TS2_TrqDem);
}
DSP 5
Custom RTOS developed in-house based on messaging
Code automatically generated to handle messaging through DPR, LinkPort, ARCNet
Compile
file .H

## Slide 23
Test Report
Target Slip Shaper was successfully used during T07 Event in Jerez:
Event | T07 |  | 
Track | Jerez |  | 
Date | 07/02/2005 |  | 
Ctrl Eng. | BL/LT/FR |  | 
Chassis | 502 | 503 | 411
Drivers | RZ/RS | JT | RZ
LT commented:
  Type used. 7 poles at around 18Hz, 0.1 damping ratio.
  Slip Overshoot. significantly less slip overshoot in almost every case in the test performed. This should result in a less snappy response for drivers like RZ whose throttle application is quite aggressive. This could also result in less snap oversteer which is what RZ complained of the most today. The reduced slip overshoot is significant and to me should result in less tyre usage, if only for a short time.
  Inside wheel oscillation. No real difference seen in the runs we tested.
  Performance implications. As can be seen in the figures below the performance of the slip shaper in not noticeably different in terms of acceleration to that of no slip shaper. However as the driver is then capable of simply flooring the throttle and not having to worry about the system snapping without loss of traction, the result is clear, maybe. In several cases, significantly, the shaper achieves the target in the same amount of time as the standard method, i.e. when there is large undershoot.

## Slide 24
Test Report
Effect of TC shaper applied (red) and not (blue). Much higher overshoot initially. Always had as good if not lower degree of overshoot.

## Slide 25
Test Report
Effect of much higher application of throttle and the corresponding shapes of the slip overshoot. In this case higher throttle is tempered by the shaper. The corresponding accelerations show no obvious difference.

## Slide 26
Test Report
Similar throttle application resulting in lower slip overshoot.

## Slide 27
Auto-tuning through GA
Use Genetic Algorithm to find shaper parameters which best fit model response
C0
T1
C1
T2
C2
Tn
Cn
…
Chromosome definition:
Fitness function definition:
err0
err1
ITERATIVE PROCESS to generate new populations:
Calculate fitness function for each chromosome of population.
Apply elitism: only two best chromosomes of each population will survive unchanged.
Apply crossover.
Apply mutation (with a specified probability).
Discard worst two chromosomes.
Apply constraints to chromosomes of new population: C and T need to be normalized => ΣCi=1, ΣTi<max.

## Slide 28
Auto-tuning through GA
GA is capable of finding parameters which fit response model in a better way with respect to theoretical parameters (with the same number of zeros):
Useful also when Plant dynamic is not known.
Run Shaper Scan
Test with 3rd order plant:
f1=17.5 Hz, ζ1=0.1
f2=20 Hz, ζ2=0.7
f3=23 Hz, ζ3=0.05

## Slide 29
References
References
Smith, O. J. M., “Posicast Control of Damped Oscillatory Systems”, Proc. of the IRE, 1957, pp 1249-1255.
W. E. Singhose, “Command Generation for Flexible Systems”, S.B.M.E., Massachusetts Institute of Technology, 1990.